## Slide 1
AGENDA · WHAT WE HAVE DONE
Reconstructing Worn Tooth Surfaces
• Goal: restore missing anatomy on worn EDJ molar surfaces (dental wear removes cusp geometry).
• Built a Statistical Shape Model (SSM) pipeline
  – Point correspondence across 15 unworn + 25 worn teeth (100k points each)
  – Per-tooth neighborhood-adaptive SSM reconstruction
• Explored several reconstruction strategies
  – Global / neighborhood SSM fit; deviation swap; correspondence blend
  – New patch-based reconstruction that fills only the worn regions
• Quantitative evaluation
  – Chamfer distance of each method vs. the ORIGINAL unworn teeth (TEST1=n0245, TEST2=n0257)
  – 8 progressive wear levels each (Molnar stages 3–6)

## Slide 2
SAMPLE RESULTS
Example Reconstructions
[ Add sample images here ]
e.g. worn input → reconstruction → overlay vs. original

## Slide 3
EVALUATION · CHAMFER DISTANCE (MM, LOWER = BETTER)
Results: Accuracy vs. the Original Tooth
Mean over all 8 wear levels
Method | TEST1 | TEST2
Patch (holes, TPS) | 0.0495 | 0.0321
Neighborhood SSM | 0.0598 | 0.0575
Correspondence blend | 0.0793 | 0.0624
Deviation swap | 0.0796 | 0.0638
Per wear level · Patch (TPS) vs SSM · Molnar 3→6
Lvl | T1 TPS | T1 SSM | T2 TPS | T2 SSM
0 | 0.0183 | 0.0491 | 0.0175 | 0.0523
1 | 0.0187 | 0.0516 | 0.0179 | 0.0524
2 | 0.0218 | 0.0532 | 0.0188 | 0.0538
3 | 0.0233 | 0.0557 | 0.0199 | 0.0537
4 | 0.0283 | 0.0583 | 0.0214 | 0.0537
5 | 0.0281 | 0.0602 | 0.0250 | 0.0539
6 | 0.0595 | 0.0851 | 0.0377 | 0.0676
7 | 0.1976 | 0.0652 | 0.0993 | 0.0729
• Patch wins at mild–moderate wear (levels 0–6); SSM wins at severe wear (level 7).
• Patch is best on mean Chamfer (~17% better than SSM on TEST1, ~44% on TEST2) — it keeps the real surface and only fills worn regions.
• Green = better (lower) of the two for that level.

## Slide 4
THE APPROACH THAT SCORED BEST
New Method: Patch-Based Reconstruction
• Idea: keep the real worn surface, restore ONLY the missing material.
• Detect worn / open-hole regions on the real scanned tooth.
• Fill each region with the SSM reconstruction as a graft:
  – Locally ICP-align the reconstruction to the worn rim around each hole
  – Fit a thin-plate-spline height field in the hole's own local frame — smooth and follows the tooth's curvature (no flat tops)
  – Match the patch density to the surrounding surface and feather the seam
  – Restrict filling to the occlusal surface — the cervical base is left open (not patched)
• Result: real detail is preserved everywhere intact; only worn cusps are rebuilt.
• Closest reconstruction to the original full tooth: 0.0495 mm (TEST1), 0.0321 mm (TEST2).